## Slide 1: Finding the Arduino
GROUP 5
Arduino/Xbee Localization System
Algorithm Used : KNN
Basic Scheme:
4 Arduino/Xbee utilized as Beacons and a mobile Xbee as the query point that we want to localize.
Use of RSSI values gathered in vector format by sending packets through node-js in estimating the location of sender Xbee.

## Slide 2: Overall Design
API mode (Enabled 2) configuration for all Xbees
Collection of RSSI values in a vectorized lookup table from all 4 Beacons
Utilized KNN Algorithm to locate Xbee on the-go by comparing the sampled RSSI values to those of the lookup table
Use of SVG to dynamically visualize the transfer of the on the-go Xbee
Included Plan for the area with 9 partitions as our base areas for positioning our mobile query

## Slide 3: KNN Algorithm
Localization was performed by assigning the moving Xbee to the class most common among its K nearest neighbors
Closeness or Proximity was defined in terms of the Euclidean Distance
Σ(Rssi(training) - Rssi (test))2
The closer the Xbee to its class means less distinction from its class K neighbors and the smaller the variance

## Slide 4: Data Flow
On the-go Xbee sends packet
Get back RSSI values from 4 Beacons
Locate on the-go Xbee with KNN algorithm
Node-js
API mode(2)
For communication with Xbees
CANVAS.JS / SVG Graphics
For visualization of updated location

## Slide 5: Overall Features
Dynamic upload of new location of moving Xbee
SVG and Canvas.js
Used Raspberry PI at server end
Mapping lookup table (training set) data to graphs
Socket.io connection for sending sampled (test data) to server